## Slide 1: The Bleeding Edge – Part I: Emerging Applications of Nanomechanics
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
It's called bleeding edge because it's science trying to make the leap into technology
And those of us working in such fields often feel bloodied in such attempts!
We can’t possibly cover the whole “bleeding edge” in one day
Today I'll highlight just 3 areas where nanomechanics might bring radical change:
1) Walking on the walls: Exploiting nano surface effects
2) DNA Erector Sets: The key to non-biological self-assembly?
3) The Beanstalk: A real stairway to the heavens?

## Slide 2: 1) Walking on the walls: Exploiting nano surface effects
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Looking for ideas we can hijack from nanoscale mother nature
This looks like it has got possibilities:
Can we emulate insect wall walking (or at least exploit their tricks?)
(from “Insects did it ﬁrst: a micropatterned adhesive tape for robotic applications”
Gorb et al., Bioinpiration & Biometrics 2 (2007))

## Slide 3: How MIGHT insects be walking on walls?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Velcro? Nano-Velcro:
No, can’t be what insects use because it IS attachment via hook AND loop
Insects could grow hooks (or loops) on their feet
But could then only climb surfaces with loops (or hooks) . . . very limiting
(from Hope Chik’s presentation on the “INEM Nano Attach Project”)

## Slide 4: Better possibility might be a nanoscale surface effect
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Effect #1: Van der Waals bonding (a.k.a. “induced dipole bonding”)
Electrons on molecules (especially longer ones) can slosh back and forth
This disrupts local charge balance setting up regions of + or -
Counter-charged nearby molecule is then attracted:
(see also my note set on Molecular Self-Assembly

## Slide 5: But VDW attraction occurs only over VERY short distances
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Because, despite charge sloshing, molecules are still net electrically neutral
So moving away from local + / - charge imbalance, forces begin to cancel
Result: For strong VDW forces, molecules must be within ~ one nanometer
But how do solid or semi-solid surfaces fit that closely together? They must be:
a) Smooth on nanoscale OR b) One piece must be ~ nanoscale
Suggesting that insects might need VERY TINY feet!

## Slide 6: And/Or insects might exploit “surface tension”
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Surface tension is also based on attraction between charge dipoles
But water's molecular dipole is permanent (unlike transient VDW charge waves)
Water molecules move/rotate to bring negative oxygen's near positive hydrogen's
Interior water molecules are happy
Many molecules at edge of droplet are not!
(e.g., prevalence of + charge on surface)
To minimize unhappy surface molecules, minimize surface area => “surface tension”

## Slide 7: To attract such water droplets to surfaces, we'll need:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Surfaces that also have polarized charge (a.k.a. “hydrophillic” surfaces)
Oxidized surfaces naturally have such polarized oxygen-to-other bonds
And they're VERY common in oxidizing atmosphere: glass, metal surfaces . . .
With only a few rotations, water molecules
on bottom of earlier water droplet are
now QUITE happy near oxide surface:

## Slide 8: So we’d guess that insects must have sweaty little polarized feet
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
And this turns out to be correct:
Small insects: Compliant pads (to shape themselves to rough surfaces) + sweat
Medium insects: Multiple pads per leg + sweat
Spiders and lizards: Lots of pads (hair) per foot - but dry / no secretions
(“From micro to nano contacts in biological attachment devices,” Arzt et al., PNAS 100(19) 2003))

## Slide 9: And applying this new found knowledge:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
We get wall climbing robots:
Supporting webpage with full Stickybot movie:
Bleeding Edge Nanomechanics - Supporting Materials - Stickybot

## Slide 10: NASA's planned use for Son of Stickybot:
Source: http://www.airspacemag.com/space/orbital-inspectors-180953376/?page=1&no-ist
The International space station gets hit by ~3000 micrometeorites per year!
Astronaut EVA’s to inspect after each of these would be costly and dangerous
Today’s fix: Proliferation of steerable cameras mounted on ISS surface
And they are working on a rocket-powered flying inspection robot
Modeled on the Star War’s light saber-training bot - "MIT SPHERES:"
But NASA believes long-term solution could be bots crawling over surface
Clinging by means of Stickybot’s Van der Waals attracted mini-haired feet:
So they hired one of the Stanford Stickybot
graduate students to develop "LEMUR"
(here represented only via computer graphics):

## Slide 11: We can also turn our knowledge around to get SUPER HYDROPHOBIC SURFACES
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
What would be required to make surfaces unattractive to water?
1) Materials w/ NON-polarized surfaces
2) Rough surfaces minimizing close contact required for Van der Waals bonding

## Slide 12: Or as shown in this computer animation of “The Lotus Effect”
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Supporting webpage with full Lotus Effect movie:
Bleeding Edge Nanomechanics - Supporting Materials - LotusEffect
(add credits)
(Source: William Thielcke, Hamburg Germany)

## Slide 13: But does reality work as well?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Yes. And you’ll get to try this out for yourself in the lab!
(Source: Neil Shirtcliffe, Nottingham Trent University / YouTube)
Supporting webpage with full YouTube video:
Bleeding Edge Nanomechanics - Supporting Materials - Hydrophobicity

## Slide 14: OK it's fun to watch, but is it useful?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
If dirty water flows quickly off surfaces, it will not dry there (leaving dirt behind)
Further, as shown in animation, droplets can pick up and carry away earlier dirt:
Dirt Dirt
APPLICATIONS: Self-cleaning windows, paints, photovoltaic solar energy panels . . .
That’s why it is called
“The Lotus Effect”
It’s a way plants keep
leaf surfaces clean!

## Slide 15: Also, why then bother with plumbing?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
There are many times when we'd like a whole analytical chemistry “lab on a chip”
This might now be possible without building mini test tubes and beakers!
We could instead could just PRINT patterns using super hydrophobic inks
Forcing water to then flow ONLY where there was no ink
(Source: Wikipedia Commons - Micronit Microfluidics Inc.)

## Slide 16: Actual operation of micro “lab on a chip” components
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Via combination of micro-machined channels and hydrophobic surface treatments:
Supporting webpage with lab on a chip videos:
Bleeding Edge Nanomechanics - Supporting Materials - Lab on a chip
(Source: Micronit Microfluidics Inc.)

## Slide 17: Or, how about a deterrent to "guys behaving badly" (in Hamburg Germany):
Link to video: http://www.slate.com/articles/video/video/2015/03/hydrophobic_paint_public_urinators_germany_rigged_walls_video.html
Walls in the red light district are being painted with hydrophobic coatings:
(before) (after)

## Slide 18: 2) DNA Erector Sets: The key to non-biological self-assembly?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Recurring obstacle to conversion of nanoscience into complex nanotechnology
is our inability to make more then a few expensive prototypes
We hope to find a solution in SELF-ASSEMBLY, but we are not sure how
One particularly exciting possibility is use of DNA outside of living organisms
Key observations:
Off-the-shelf equipment can now create programmed DNA strands
Complementary DNA segments separate (“denature”) w/ mild heat (~90 ˚C)
Then naturally recombine upon cooling

## Slide 19: What if one strand is coded to complement parts of two others?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Create the following three synthetic DNA single strands:
What is going to happen if they are mixed together then cooled?
~ 90 ˚C < 80 ˚C

## Slide 20: And it is just about that simple:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Start with four encoded strands, Although the atomistic reality
cool in solution to assemble together: is a bit more twisted:
Four single strands of DNA combine to form "Holliday” X junctions (Wikipedia Commons)
Resulting 3D DNA structure
(Richard Wheeler - Wikipedia Commons)

## Slide 21: As confirmed by high resolution electron microscopy:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Each node of this nanoscale mesh was fabricated as shown on preceding slide:
The pioneer of this field,
Ned Seeman of New York Univ.
assured me it is really ~ that easy!
(Thomas H. LaBean & Hao Yan - Wikipedia Commons)

## Slide 22: Ned Seeman has taken it into 3D:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Schematic of 3D box: Complete DNA structure:
Based on the work of Ned Seeman, New York University
(See Ned Seeman papers at Bleeding Edge Nanomechanics – Supporting Materials - DNA Scaffolding)

## Slide 23: Why as an electrical engineer does this excite me?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Possibility of Using DNA self-assembly to:
1) Arrange DNA boxes into scaffolds
2) But with extra single strand DNA “address label” ends in each box
3) Then add quantum dots with complementary single strands => Q-Dot arrays!

## Slide 24: Or in 3D:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Based on DNA scaffold, Q-dots self-assemble into programmable 3D arrangement:
Different DNA scaffolds => Different 3D Q-dot structures!
("Nanotechnology and the Double Helix"
Scientific American 2007)

## Slide 25: But is this just another artwork fantasy?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
No!
Here's an electron micrograph Ned Seeman
sent me of such DNA organized Q-dot array:
Along the lines of this classic cartoon
lampooning scientists' wishful thinking?
By Sidney Harris:

## Slide 26: An alternate approach based on DNA rafts:
Lay out long, standard, well-known strand of bacterial DNA in desired shape (black line)
Link its turns together with short engineered complementary strands
"DNA Origami"
(See Paul Rothemund paper at Bleeding Edge Nanomechanics – Supporting Materials - DNA Origami)

## Slide 27: Or in 3D, taking DNA spiral into account:
Sounds easy? Think again!

## Slide 28: The dirty little details
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Step 1 (in design process) – DNA double strand folded back on itself:
Natural point to make a new link
Place where red (secondary / non-master) strand comes into close alignment

## Slide 29: The dirty little details (cont'd)
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Step 2 – Cut secondary strand at this point:
But how should severed strands now be cross-connected?
New connections MUST take into account direction (5' => 3') of DNA backbone
Making sure that connection maintains this progression (see arrows)
NO! YES!

## Slide 30: The dirty little details (cont'd)
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Step 3 – Connect up what becomes a "staple" cross-connection segment:
New red = Staple segment
Blue & Yellow = non-staple segments
OR if merge blue/yellow at appropriate point, they could become second staple

## Slide 31: Oh, but I forgot something major:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
We can't just arbitrarily link strands!
Backbone units of (phosphate + ribose) must repeat every 1/10 turn
Position of cuts and reconnections MUST maintain this repetition
So can one indeed add short (single phosphate-ribose) link as I show above?
THAT ribose would have to do without an attached base
It that feasible? Or must link be deleted, pulling DNA strands very tightly together?
This problem must be solved, one way or another, to get to final step:
Step 4 – Choose BASES on colored segments to complement
opposing BASES on black bacterial master strand

## Slide 32: Sounds like design might require one heck of a computer program
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Which might explain why its inventor, Paul Rothemund in NOT a biologist
Nor is he a nanoscientist (at least, not a conventional one)
Rothemund IS in fact a Computer Science professor
But then does he only plan (a.k.a. "model") such things?
And should we really trust that those plans are viable?
That his programs get all of the above details right?
And that proposed bending of DNA is actually feasible?

## Slide 33: Here's the proof: He also makes these things:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Source: Folding DNA to create nanoscale shapes and folding patterns, P.W.K. Rothemund, Nature 440, p297 (2006)
Figures
Data

## Slide 34: And flat DNA rafts can also be folded into 3D shapes:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Start with planar DNA Origami raft, the add cross links to fold the raft into a 3D shape:
NOW do you understand why EE professors like me are studying DNA?
Take one whole week for very SLOW cooling
Giving time for raft to fold and unfold,
Allowing links to bump into one another and connect up!
(See Shawn Douglas paper at Bleeding Edge Nanomechanics – Supporting Materials - DNA Origami)

## Slide 35: The design programming sounds REALLY complex
www.cadnano.org
But there is now a free, downloadable, do-it-yourself DNA Origami design program!
Developed by the Dana Farber Cancer Lab & Harvard's Wyss Institute

## Slide 36: There is a somewhat related effort to use DNA to "compute"
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Generally, to compute solutions to "combinatorial" problems
For instance, finding the most effective complex routes
Where there is a HUGE range of possible route segments
Classic problem is how to go through a large number of points via fewest lines
But some complete routes
are a LOT shorter than others!

## Slide 37: Computers can't cope with humongous number of possible routes!
Because number of routes increases as factorial of number of connecting points (n!)
So, instead, associate each possible point ("node") with a DNA base pair sequence:
Then create a DNA segments with "sticky ends" coded to each node:
Coded "sticky ends" will then drive those "connectors" to connect those nodes:
Node 1:
Node 2:
">1-2>"
">2-3>"
Node 3:
Node 1:
Node 3:
Node 2:

## Slide 38: Now synthesize connectors for EVERY possible connection
For the earlier route drawing you'd need at least these connectors:
>0-1>, >0-3>, >0-6>, >2-1>, >2-3>, >3-4>, >4-1>, >4-5>, >5-1>, >5-6>
Then make a huge number of copies of each connector
As you will see in our DNA lab, you can just use "PCR multiplication"
Mix everything together, heat above 90°C, then slowly cool:
You'll connect long strings of DNA, representing EVERY possible route
Sort those strings by length, using standard "gel electrophoresis" technique
Shortest one has smallest number of connectors
Decode its connectors' identity and positions => Shortest possible route!
Seminal publication (and route figure) was by Aldeman (in 1994)
Copy, plus some explanatory notes, are posted on Supporting Webpage

## Slide 39: 3) The Beanstalk: A real stairway to the heavens?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
I used to have lecture on the huge flaws in many nano science fiction stories
But, strangely, Nano may soon make one of Sci-Fi's BIGGEST ideas possible:
The “Beanstalk”
Proposed by Arthur C. Clarke in his 1979 novel "The Fountains of Paradise"
But what is a Beanstalk?

## Slide 40: This is a Beanstalk:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Also known as a “Skyhook” or as a “Space Elevator”
Google images: http://www.blog.speculist.com/archives/2004_12.html

## Slide 41: It’s actually an old idea . . . But with a BIG problem
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
It was proposed by Russian scientist Konstantin Tsiolkovsky, in 1895
Satellite’s orbit = balance between centrifugal force & gravitational force
Higher it goes, weaker the gravity, slower the orbit required
Near-earth orbit (R ~ 6,500 km) ~ 90 minutes
Moon orbit (R ~ 385,000 km) ~ 30 days
35,786 km orbit = one day → Over equator, stays above fixed point = “Geosynchronous Orbit”
Tsiolkovsky: Satellite is happy, earth is happy, tie together with rope + elevator
Problem: Rope is not happy, all but top of it is moving too low and slow to orbit
Load on rope => Good fraction of its own 35,000 km length => SNAP!
So you'll need incredibly LIGHT yet STRONG rope!!!

## Slide 42: Analysis by U. Washington Physics Prof. John G. Cramer:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
In his December 2001 Alternate View column in Analog Magazine (link to cached copy)
Tension at top of rope = 92 Giga Pascals = 13.3 MILLION pounds per square inch!
But he also estimates that: Carbon nanotube (CNT) rope might attain strength 50% larger!
HOWEVER: 36,000 km long single carbon nanotubes cannot now be grown
Even ONE continuous METER is beyond our current capability
So Cramer invoked rope woven from short fibers (like normal rope)
This assumes bonds between CNTs are as strong as bonds within CNTs
That's NOT the case with normal fibers, nor presently the case with CNTs
So how MIGHT this be done?

## Slide 43: My thoughts about ways of linking carbon nanotubes
Scheme 1) Splice together with larger nanotubes:
Might pull this off once (= enough for another AZOnano headline?) . . . but a gazillion times?
Scheme 2) Bond together via intermediate atoms or molecules:
But carbon-other bonds are SO much weaker than carbon-carbon bonds!!
Scheme 3) Bond together the carbon atoms on adjacent nanotubes
Let's explore this one a bit more deeply:

## Slide 44: Direct carbon to carbon nanotube binding:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Need to go from carbons bonded with 3 neighbors to bonding with four neighbors
Graphene Diamond
(3 neighbors): (4 neighbors):
Both DO have exceptionally strong bonds! Take a closer look at diamond:
Need to incorporate some of these structures into the surface of graphene:

## Slide 45: Diamond bonding inserted into graphene sheet:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Bonds DO bend fairly easily, so that part might be plausible
But it is MUCH harder to stretch bonds (as I did in these figures):
So I don't know if depicted configuration is energetically feasible
And I worry about disruption of graphene's "resonant bonding" (use of 4th electrons)
But assume this IS energetically feasible and CAN be induced:
Need to go from carbons bonded with 3 neighbors to bonding with four neighbors

## Slide 46: Possible result:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
So this might provide a way of linking short carbon nanotubes together
But Cramer’s estimate of CNT strength = 3-10 times larger than figure I got from other experts
However numbers ARE in the ballpark, and “experts” have been wrong or superseded before
(i.e. I wouldn’t invest in beanstalk / skyhook yet, but not sure I’d bet against it either)

## Slide 47: Conclusions
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Discussed (only!): Walking on the walls
DNA Erector Sets
Beanstalks / Skyhooks
Only a few of many “bleeding edge” mechanical applications of nanotechnology
Nevertheless, range of potential applications is already stunning
Next week: Bleeding edge of nanoelectronic applications

## Slide 48: Credits / Acknowledgements
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Funding for this class was obtained from the National Science Foundation (under their Nanoscience Undergraduate Education program).
This set of notes was authored by John C. Bean who also created all figures not explicitly credited above.
Copyright John C. Bean
(However, permission is granted for use by individual instructors in non-profit academic institutions)